## Slide 1: Hardware Software Platforms Project Presentation
Measuring temperature on TMP100
NAJI Doha (doha.naji@student.umons.ac.be)
HOEDENAEKEN Clément
(clement.hoedenaeken@student.umons.ac.be)

## Slide 2: Table of contents
A) Introduction
B) Steps of the design
1. I2C driver
2. Bloc (control state machine)
3. Main.c (data => PC)
C) Demonstration video
E) Conclusion

## Slide 3: A) Introduction
Objective : create a tutorial based on Quartus and DE0 kits
interaction with peripheral
Control driver and interaction with the environment

## Slide 4: B) Steps of the design

## Slide 5
1. I2C driver : context
* Implemented on FPGA in VHDL
* Pilots the TMP100 Temperature Sensor
* Uses I2C protocol and bus

## Slide 6
Half-duplex bidirectional synchronous serial bus
One bit sent at a time
Clock signal to synchronize the communication
Communication possible in both direction
One element speaks at a time
2 wire-interface:
1 wire for the Data : SDA
1 wire for the Clock : SCL
+ 2 for power supply
1. I2C driver : I2C protocol and bus

## Slide 7
The first who takes the control of the bus becomes the master. It generates the start Condition. The other one becomes the slave.
Star Condition
SDA
1
0
Stop Condition
SCL
0
1
SDA
1
1
SCL
(Bus busy)
(Bus free)
1. I2C driver : I2C protocol and bus

## Slide 8
1) Master
1. I2C driver : I2C protocol and bus
Slave
Start Condition : The master puts the line to 0 + generation of the clock
At each rising edge, sending of a bit of the slave address (8 bits : 8th bit = R/W)
The master puts the line to 1 untill the slave puts the line back to 0 (ACK) : the communication begins at the next rising edge.
The master puts the line to 1 untill the slave puts it back to 0:
ACK --> Stop Condition

## Slide 9
2) Slave
1. I2C driver : I2C protocol and bus
Master
Start Condition (similary to the master/slave communication)
At each rising edge, sending of a bit of the address of the slave
The Master puts the line into1 untill the slave puts back the line to zéro (ACK) + sending of the data
The slave puts the line to 1 untill the master puts the line back to 0 : ACK --> Stop Condition

## Slide 10
Start condition
Slave address writing
Writing loop
Reading loop
End condition
1. I2C driver : I2C protocol and bus

## Slide 11
Writing the configuration
Connecting the temperature register
Reading the temperature
(Given by the sensor datasheet)
1. I2C driver : I2C protocol and bus

## Slide 12
  Slave address : 1001 000
  Configuration of the sensor : 12 bits
Write address of config register
Write the config (01100000)
Write the address of temp register
Read temp register
1. I2C driver : configuration of the sensor

## Slide 13
Writing the configuration
Writing connecting the temperature register
Reading the temperature
Delay : min 320 ms
1. I2C driver : the signals we want to produce

## Slide 14
2. Bloc (control state machine)
State machine to control the I2C driver and process the data

## Slide 15
Objective : Drive this state machine (follow the colored paths)
Action : Place values in the registers and activate right signals at the right moment (e.g. : enable, rw,…)
Help : Flags raised by the machine (e.g. : busy, val_rdy, reg_rdy,…)
2. Bloc (control state machine)

## Slide 16
2. Bloc (control state machine)

## Slide 17
Writing the configuration
Writing connecting the temperature register
Reading the temperature
2. Bloc (control state machine) : testing it with a testbench

## Slide 18
Serial Protocol Communication
ARM
SoC
FPGA
3. Main.C
Terminal/Putty
Terminal/Putty

## Slide 19: C) Demonstration video

## Slide 20: D) Conclusion
 | Working | Tested
Driver I²C | ✅ | Modelsim : ✅
Control State Machine (Bloc) | ❌ (clock not working) | Modelsim :✅ Oscilloscope : ❌
Code in C | ✅ (reads « 0°C ») | ✅

## Slide 21
Thank you !
Questions?